## Slide 1: Computer and Robot Vision I
Chapter 11
Arc Extraction and Segmentation
Presented by: 鄭鴻鈞
b09902134@ntu.edu.tw
授課教授：傅楸善 博士

## Slide 2: 11.1 Introduction
In some image sets, lines, curves, and circular arcs are more useful than regions or helpful in addition to regions.
  object recognition
  stereo matching
  document analysis
2

## Slide 3: 11.1 Introduction
In this Ch., we discuss techniques for extracting sequences of pixels that belong to the same curve.
  Source: a segmented or
  labeled image
3

## Slide 4: 11.1 Introduction
Grouping Operation :
After edge labeling or image segmentation
To extract sets or sequences of labeled or border pixel positions.
The extracted pixel’s positions:
belong to the same curve (group)
sequence of pixels group features
4

## Slide 5: 11.1 Introduction
Labeling
edge detection: label each pixel as edge or not
additional properties: edge direction, gradient magnitude, edge contrast….
Grouping
grouping operation: edge pixels participating in the same region boundary are grouped together into a sequence.
boundary sequence simple pieces
analytic descriptions shape-matching
5

## Slide 6: 11.2 Extracting Boundary Pixels from a Segmented Image
Regions have been determined by segmentation or connected components
boundary of each region can be extracted
Boundary extraction for small-sized images:
scan through the image  first border of each region
first border of each region  follow the border of the connected component around in a clockwise direction until reach itself
6

## Slide 7: 11.2 Extracting Boundary Pixels from a Segmented Image
Boundary extraction for small-sized images:
 memory problems; for large-sized one, simple border-tracking algo. may result in excessive I/O to storage
    4K UHD – (3840 × 2160) ~= 8.3M pixel
    Many techniques like down-sampling
    It may be a problem back to 1992; how about TODAY?
Border-tracking algorithm: border
Input: symbolic image
Output: a clockwise-ordered list of the coordinates of its border pixels
In one left-right, top-bottom scan through the image
During execution,
there are 3 sets of regions: current, past, future
7

## Slide 8: 11.2.2 Border-Tracking Algorithm
Past region: null
Current region: 2
Future region: 1
8

## Slide 9: 11.2.2 Border-Tracking Algorithm
Past region: 1
Current region: 2
Future region: null
9

## Slide 10
10

## Slide 11: 11.2.2 Border-Tracking Algorithm
11

## Slide 12: 11.2.2 Border-Tracking Algorithm
12

## Slide 13: 11.2.2 Border-Tracking Algorithm
(active)
13

## Slide 14: 11.2.2 Border-Tracking Algorithm
(Inactive) CHAINSET (2) -> (2,5) -> (2,6)
(active) CHAINSET (1) -> (3,2)
(3,2) NEIGHB (3,3), (4,2)
14

## Slide 15: 11.2.2 Border-Tracking Algorithm
(Inactive) CHAINSET (2) -> (2,5) -> (2,6)
(active) CHAINSET (1) -> (3,2)
- (3,3) NEIGHB (3,2),(3,4),(4,3)
- (active) CHAINSET (1) -> (3,2) -> (3,3)
15

## Slide 16: 11.2.2 Border-Tracking Algorithm
(Inactive) CHAINSET (2) -> (2,5) -> (2, 6)
(active) CHAINSET (1) -> (3,2) -> (3,3)
- (3,4) NEIGHB (3,3),(4,4)
- (active) CHAINSET (1) -> (3,2) -> (3,3) -> (3,4)
16

## Slide 17: 11.2.2 Border-Tracking Algorithm
(Inactive) CHAINSET (2) -> (2,5) -> (2,6)
(inactive) CHAINSET (1) -> (3,2) -> (3,3) -> (3,4)
(active) CHAINSET (2) -> (3,5)
(3,5) NEIGHB (2,5), (3,6), (4,5)
17

## Slide 18: 11.2.2 Border-Tracking Algorithm
(inactive) CHAINSET (2) -> (2,5) -> (2,6)
(inactive) CHAINSET (1) -> (3,2) -> (3,3) -> (3,4)
(active) CHAINSET (2) -> (3,5)
- (3,6) NEIGHB (2,6), (3,5), (4,6)
- active CHAINSET change! (clockwise-ordered)
- (active) CHAINSET (2) -> (2,5) -> (2,6) -> (3,6)
18

## Slide 19: 11.2.2 Border-Tracking Algorithm
(active) CHAINSET (1) -> (4,2)
(4,2) NEIGHB (3,3),(4,3),(5,2)
(inactive) CHAINSET (2) -> (2,5) -> (2,6) -> (3,6)
(inactive) CHAINSET (1) -> (3,2) -> (3,3) -> (3,4)
(inactive) CHAINSET (2) -> (3,5)
19

## Slide 20: 11.2.2 Border-Tracking Algorithm
(inactive) CHAINSET (2) -> (2,5) -> (2,6) -> (3,6)
(inactive) CHAINSET (1) -> (3,2) -> (3,3) -> (3,4)
(inactive) CHAINSET (2) -> (3,5)
(active) CHAINSET (1) -> (4,2)
20

## Slide 21: 11.2.2 Border-Tracking Algorithm
……………………………
21

## Slide 22: 11.2.2 Border-Tracking Algorithm
22

## Slide 23: 11.2.2 Border-Tracking Algorithm
CHAINSET
(1)(3,2)(3,3)(3,4)(4,4)(5,4)
(1)(4,2)(5,2)(5,3)
(2)(2,5)(2,6)(3,6)(4,6)(5,6)(6,6)
(2)(3,5)(4,5)(5,5)(6,5)
CHAINSET
(1)(3,2)(3,3)(3,4)(4,4)(5,4)(5,3)(5,2)(4,2)
(2)(2,5)(2,6)(3,6)(4,6)(5,6)(6,6)(6,5)(5,5) (4,5)(3,5)
23

## Slide 24: 11.2.2 Border-Tracking Algorithm
24

## Slide 25: 11.3 Linking One-Pixel-Wide Edges or Lines
Border tracking: each border bounded a closed region  NO point would be split into two or more segments.
Tracking symbolic edge (line) segments: more complex
 value:1 edge; 0: non-edge
 not necessary for edge pixels to bound closed regions
 segments consist of connected edge pixels that go from endpoint, corner, or junction to endpoint, corner, or junction.
-> pixeltype() is more complex
25

## Slide 26: 11.3 Linking One-Pixel-Wide Edges or Lines
*INLIST, OUTLIST
26

## Slide 27: 11.3 Linking One-Pixel-Wide Edges or Lines
pixeltype()  determines a pixel point
  isolated point
  starting point of an new segment
  interior pixel of an old segment
  ending point of an old segment
  junction
  corner
Instead of past, current, future regions, there are past, current, future segments.
27

## Slide 28
28

## Slide 29: 11.3 Linking One-Pixel-Wide Edges or Lines
29

## Slide 30: 11.3 Linking One-Pixel-Wide Edges or Lines
30

## Slide 31: 11.3 Linking One-Pixel-Wide Edges or Lines
31

## Slide 32: 11.3 Linking One-Pixel-Wide Edges or Lines
32

## Slide 33: 11.3 Linking One-Pixel-Wide Edges or Lines
33

## Slide 34: 11.3 Linking One-Pixel-Wide Edges or Lines
34

## Slide 35: 11.3 Linking One-Pixel-Wide Edges or Lines
35

## Slide 36: 11.3 Linking One-Pixel-Wide Edges or Lines
36

## Slide 37: 11.3 Linking One-Pixel-Wide Edges or Lines
37

## Slide 38: 11.3 Linking One-Pixel-Wide Edges or Lines
38

## Slide 39: 11.3 Linking One-Pixel-Wide Edges or Lines
39

## Slide 40: 11.3 Linking One-Pixel-Wide Edges or Lines
40

## Slide 41: 11.3 Linking One-Pixel-Wide Edges or Lines
41

## Slide 42: 11.3 Linking One-Pixel-Wide Edges or Lines
42

## Slide 43: 11.3 Linking One-Pixel-Wide Edges or Lines
43

## Slide 44: 11.4 Edge and Line Linking Using Directional Information
Previous edge_track : no directional information
In this section, assume each pixel is marked to indicate whether it is an edge (line):
  Yes, there is an associated angular direction
    pixels that have similar enough directions can form connected chains and be identified as an arc segment.
      The arc has a good fit to a simple curvelike line
  No
44

## Slide 45: 11.4 Edge and Line Linking Using Directional Information
The linking process -> scan the labeled edge image in top-down, left-right and if a labeled pixel has:
  No previous labeled neighbors
    It begins a new group
  One previous labeled neighbors
    T-test
  Two or more previous labeled neighbors
    T-test
    Merge test
45

## Slide 46: 11.4 Edge and Line Linking Using Directional Information
No previous labeled neighbors:
  initialize the scatter of group ->
: priori variance
: # of pixels
46

## Slide 47: 11.4 Edge and Line Linking Using Directional Information
If an encountered label pixel has previously encountered labeled neighbors: Measure t-statistic
47

## Slide 48: 11.4 Edge and Line Linking Using Directional Information
If the pixel is added to the group; the mean and scatter of the group are updated:
48

## Slide 49: 11.4 Edge and Line Linking Using Directional Information
49

## Slide 50: 11.4 Edge and Line Linking Using Directional Information
If there are two or more previously encountered labeled neighbors,
50

## Slide 51: 11.4 Edge and Line Linking Using Directional Information
then merge two groups
Create a new group having:
51

## Slide 52: 11.5 Segmentation of Arcs into Simple Segments
Arc segmentation: partition
extracted digital arc sequence  digital arc subsequences (each is a maximal sequence that can fit a straight or curve line)
Simple arc segment: straight-line or curved-arc segment
The endpoints of the subsequences are called corner points or dominant points.
52

## Slide 53: 11.5 Segmentation of Arcs into Simple Segments
Identification of all locations:
  (a) have sufficiently high curvature
  (b) are enclosed by different lines and curves
techniques: iterative endpoint fitting and splitting, using tangent angle deflection, or high curvature as basis of the segmentation
53

## Slide 54: 11.5.1 Iterative Endpoint Fit and Split
To segment a digital arc sequence into subsequences that are sufficiently straight.
one distance threshold d*
L={(r,c)| αr+βc+γ=0} where |(α,β)|=1
  The straight line composed by 2 endpoints of this arc
di=| αri+βci+γ | / |(α,β)| = | αri+βci+γ |
  The length of the perpendicular line composed by any single pixel of this arc and L
dm=max(di)
If dm> d* , then split at the point (rm,cm)
54

## Slide 55: 11.5.1 Iterative Endpoint Fit and Split
55

## Slide 56: 11.5.1 Iterative Endpoint Fit and Split
L
dm=max(di)
56

## Slide 57: 11.5.1 Iterative Endpoint Fit and Split
L
dm=max(di)
57

## Slide 58: 11.5.1 Iterative Endpoint Fit and Split
Circular arc sequence
  initially split by two points apart in any direction
Sequence only composed of two line segments
  Golden section search
58

## Slide 59: 11.5.2 Tangential Angle Deflection
To identify the locations where two line segments meet and form an angle.
an(k)=(rn-k – rn , cn-k - cn)
bn(k)=(rn – rn+k , cn –cn+k)
59

## Slide 60: 11.5.2 Tangential Angle Deflection
60

## Slide 61: 11.5.2 Tangential Angle Deflection
(rn-k – rn , cn-k - cn)
(rn – rn+k , cn –cn+k)
61

## Slide 62: 11.5.2 Tangential Angle Deflection
(rn-k – rn , cn-k - cn)
(rn – rn+k , cn –cn+k)
an(k)
bn(k)
62

## Slide 63: 11.5.2 Tangential Angle Deflection
At a place where two line segments meet
 the angle will be larger  cosθn(kn) smaller
A point at which two line segments meet
cosθn(kn) < cosθi(ki) for all i,|n-i| ≦ kn/2
k=?
63

## Slide 64: 11.5.3 Uniform Bounded-Error Approximation
segment arc sequence into maximal pieces whose points deviate ≤ given amount
optimal algorithms: excessive computational complexity
64

## Slide 65: 11.5.3 Uniform Bounded-Error Approximation
65

## Slide 66: 11.5.4 Breakpoint Optimization
after an initial segmentation: shift breakpoints to produce a better arc segmentation
first  shift odd final point (i.e. even beginning point) and see whether the max. error is reduced by the shift.
If reduced, then keep the shifted breakpoints.
then shift even final point (i.e. odd beginning point) and do the same things.
66

## Slide 67: 11.5.4 Breakpoint Optimization
67

## Slide 68: 11.5.5 Split and Merge
first: split arc into segments with the error sufficiently small
second: merge successive segments if resulting merged segment has sufficiently small error
third: try to adjust breakpoints to obtain a better segmentation
repeat: until all three steps produce no further change
68

## Slide 69: 11.5.5 Split and Merge
69

## Slide 70: 11.5.6 Isodata Segmentation
Iterative Selforganizing Data Analysis Techniques Algorithm
iterative isodata line-fit clustering procedure: determines line-fit parameter
then each point assigned to cluster whose line fit closest to the point
70
Notes: http://img.rritw.com/2013-01-17/1358350718_8022.gif

## Slide 71: 11.5.6 Isodata Segmentation
71
Notes: http://img.rritw.com/2013-01-17/1358350718_8022.gif

## Slide 72: 11.5.6 Isodata Segmentation
72

## Slide 73: 11.5.6 Isodata Segmentation
73

## Slide 74: 11.5.7 Curvature
The curvature is defined at a point of arc length s along the curve by
Δs : the change in arc length
Δθ : the change in tangent angle
74

## Slide 75: 11.5.7 Curvature
natural curve breaks: curvature maxima and minima
curvature passes through zero: local shape changes from convex to concave
75

## Slide 76: 11.5.7 Curvature
surface elliptic: when limb in line drawing is convex
surface hyperbolic: when its limb is concave
surface parabolic: wherever curvature of limb zero
76

## Slide 77: 11.5.7 Curvature
Nalwa, A Guided Tour of Computer Vision, Fig. 4.14 􀀀
77

## Slide 78: 11.6 Hough Transform
Hough Transform: method for detecting straight lines and curves on gray level images.
Hough Transform: template matching
The Hough transform algorithm requires an accumulator array whose dimension corresponds to the number of unknown parameters in the equation of the family of curves being sought.
78

## Slide 79: Finding Straight-Line Segments
Line equation  y=mx+b
point  (x,y)
slope  m , intercept  b
x
y
b
m
1=m+b
．(1,1)
79

## Slide 80: Finding Straight-Line Segments
Line equation  y=mx+b
point  (x,y)
slope  m , intercept  b
x
y
b
m
1=m+b
．(2,2)
．(1,1)
2=2m+b
80

## Slide 81: Finding Straight-Line Segments
Line equation  y=mx+b
point  (x,y)
slope  m , intercept  b
x
y
b
m
1=m+b
．(2,2)
．(1,1)
2=2m+b
(1,0)
y=1*x+0
81

## Slide 82: Example
．
x
y
b
m
(1,1)
．
．
．
．
(1,1)
(1,0)
(0,1)
(2,1)
(3,2)
(1,0)
(2,1)
(3,2)
(0,1)
82

## Slide 83: Example
．
x
y
b
m
(1,1)
．
．
．
．
(1,1)
(1,0)
(0,1)
(2,1)
(3,2)
(1,0)
(2,1)
(3,2)
(0,1)
(0,1)
(1,-1)
y=1
y=x-1
83

## Slide 84: Finding Straight-Line Segments
Vertical lines  m=∞  doesn’t work
d : perpendicular distance from line to origin
θ : the angle the perpendicular makes with the x-axis (column axis)
84

## Slide 85: Finding Straight-Line Segments
．(dsinθ,dcosθ)
．(r,c)
Θ
Θ
Θ
85

## Slide 86: Example
r
c
86

## Slide 87
87

## Slide 88
88

## Slide 89: Example
．
y
．
．
．
．
(1,1)
(1,0)
(0,1)
(2,1)
(3,2)
x
．
r
．
．
．
．
(1,1)
(0,1)
(1,0)
(1,2)
(2,3)
c
89

## Slide 90: Example
．
r
．
．
．
．
(1,1)
(0,1)
(1,0)
(1,2)
(2,3)
c
 | -45° | 0° | 45° | 90°
(0,1) | 0.707 | 1 | 0.707 | 0
(1,0) | -0.707 | 0 | 0.707 | 1
(1,1) | 0 | 1 | 1.414 | 1
(1,2) | 0.707 | 2 | 2.121 | 1
(2,3) | 0.707 | 3 | 3.535 | 2
90

## Slide 91: Example
accumulator array
 | -0.707 | 0 | 0.707 | 1 | 1.414 | 2 | 2.121 | 3 | 3.535
-45° | 1 | 1 | 3 | - | - | - | - | - | -
0° | - | 1 | - | 2 | - | 1 | - | 1 | -
45° | - | - | 2 | - | 1 | - | 1 | - | 1
90° | - | 1 | - | 3 | - | 1 | - | - | -
 | -45° | 0° | 45° | 90°
(0,1) | 0.707 | 1 | 0.707 | 0
(1,0) | -0.707 | 0 | 0.707 | 1
(1,1) | 0 | 1 | 1.414 | 1
(1,2) | 0.707 | 2 | 2.121 | 1
(2,3) | 0.707 | 3 | 3.535 | 2
91

## Slide 92: Example
accumulator array
 | -0.707 | 0 | 0.707 | 1 | 1.414 | 2 | 2.121 | 3 | 3.535
-45° | 1 | 1 | 3 | - | - | - | - | - | -
0° | - | 1 | - | 2 | - | 1 | - | 1 | -
45° | - | - | 2 | - | 1 | - | 1 | - | 1
90° | - | 1 | - | 3 | - | 1 | - | - | -
．
r
．
．
．
(1,1)
(0,1)
(1,0)
(1,2)
(2,3)
c
．
92

## Slide 93: Example
accumulator array
 | -0.707 | 0 | 0.707 | 1 | 1.414 | 2 | 2.121 | 3 | 3.535
-45° | 1 | 1 | 3 | - | - | - | - | - | -
0° | - | 1 | - | 2 | - | 1 | - | 1 | -
45° | - | - | 2 | - | 1 | - | 1 | - | 1
90° | - | 1 | - | 3 | - | 1 | - | - | -
．
r
．
．
．
(1,1)
(0,1)
(1,0)
(1,2)
(2,3)
c
．
93

## Slide 94: Finding Straight-Line Segments
94

## Slide 95: Finding Circles
: row
: column
: row-coordinate of the center
: column-coordinate of the center
: radius
: implicit equation for a circle
95

## Slide 96: Finding Circles
96

## Slide 97: Extensions
The Hough transform method can be extended to any curve with analytic equation of the form , where denotes an image point and is a vector of parameters.
97

## Slide 98: 11.7 Line Fitting
 points before noise perturbation
 lie on the line
 noisy observed value

 independent and identically distributed with mean 0 and variance
98

## Slide 99: 11.7 Line Fitting
procedure for the least-squares fitting of line to observed noisy values
principle of minimizing the squared residuals under the constraint that
Lagrange multiplier form:
99
Notes: http://episte.math.ntu.edu.tw/entries/en_lagrange_mul/

## Slide 100: 11.7 Line Fitting
→
→
→
100

## Slide 101
→
→
→
101

## Slide 102: 11.7.2 Principal-Axis Curve Fit
The principal-axis curve fit is obviously a generalization of the line-fitting idea.
The curve
e.g. conics :
102

## Slide 103: 11.7.2 Principal-Axis Curve Fit
The curve
minimize

103

## Slide 104: 11.8 Region-of-Support Determination
region of support too large: fine features smoothed out
region of support too small: many corner points or dominant points produced
        k=?
104
Notes: k個有序前點和k個有序後點組成的一個邊緣片段稱為點的2k+1支撐區域。

## Slide 105: 11.8 Region-of-Support Determination
Teh and Chin
  Calculate , until
  Region of support:
105
Notes: http://www.ecice06.com/CN/article/downloadArticleFile.do?attachType=PDF&id=13978

## Slide 106: 11.9 Robust Line Fitting
Fit insensitive to a few outlier points
Give a least-squares formulation first and then modify it to make it robust.
106
Notes: iteratively

## Slide 107: 11.9 Robust Line Fitting
In the weighted least-squares sense:
107

## Slide 108: 11.10 Least-Squares Curve Fitting
Determine the parameters of the curve that minimize the sum of the squared distances between the noisy observed points and the curve.
108

## Slide 109: 11.10 Least-Squares Curve Fitting
‧
‧
109

## Slide 110: 11.10 Least-Squares Curve Fitting
‧
‧
‧
110

## Slide 111: 11.10 Least-Squares Curve Fitting
→
→
→
111

## Slide 112: 11.10 Least-Squares Curve Fitting
Distance d between and the curve :
112

## Slide 113: 11.10.1 Gradient Descent
113
Notes: 一個函數的梯度方向是增大最陡的方向
梯度方向是一個函數變化最劇烈的方向。也就是沿著這個方向你移動L的距離得到的函數值變化是最大的。

## Slide 114: 11.10.1 Gradient Descent
First-order iterative technique in minimization problem
Initial value :
(t+1)-th iteration 
First-order Taylor series expansion around
should be in the negative gradient direction
114

## Slide 115: 11.10.2 Newton Method
Second-order iterative technique in minimization problem
Second-order Taylor series expansion around
 second-order partial derivatives, Hessian
Take partial derivatives to zero with respect to
115
Notes: http://ccjou.wordpress.com/2013/09/09/%E7%AD%94%E5%BC%B5%E7%9B%9B%E6%9D%B1%E2%94%80%E2%94%80%E9%97%9C%E6%96%BC-hessian-%E7%9F%A9%E9%99%A3%E8%88%87%E5%A4%9A%E8%AE%8A%E9%87%8F%E5%87%BD%E6%95%B8%E7%9A%84%E6%B3%B0%E5%8B%92%E5%B1%95%E9%96%8B/
http://zh.wikipedia.org/wiki/%E6%B5%B7%E6%A3%AE%E7%9F%A9%E9%98%B5

## Slide 116: 11.10.4 Fitting to a Circle
Circle :
116

## Slide 117: 11.10.4 Fitting to a Circle
117

## Slide 118: 11.10.6 Fitting to a Conic
In conic :
118

## Slide 119: 11.10.3 Second-Order Approximation to Curve Fitting
==Nalwa, A Guided Tour of Computer Vision, Fig. 4.15== 􀀀
119

## Slide 120: 11.10.9 Uniform Error Estimation
Nalwa, A Guided Tour of Computer Vision, Fig. 3.1 􀀀
120

## Slide 121
The End