## Slide 1: Hand gesture recognition
Presenter:藍泓景
E-mail:r12922134@ntu.edu.tw
Phone:0908013956

## Slide 2: The Concept of Smart Glasses
Hardware
Virtual Reality (VR) and Augmented Reality (AR)
Interacting with Smart Glasses

## Slide 3: Virtual Reality (VR) and Augmented Reality (AR)
Mixed Reality (MR) is a “virtuality continuum”,
AR is a subset of MR.
(Milgram & Kishino, 1994)

## Slide 4: The Method of Depth Estimation
Time of Flight
Resolving distance between the camera and the object for each point of the image.
Provided by a laser or a Light Emitting Diode (LED).

## Slide 5: Our Hardware Configuration
Smart glasses: Jorjin J7EF Plus
Smartphone: Sony Xperia 1 II
Operating System (OS): Android 12
Jorjin J7EF Plus
  FoV: (horizontal)
  Display resolution: 1080p
  Inter-Pupillary Distance (IPD): 65 mm
  Sensors:
    8 MP RGB camera
    64 (=8 x 8) pixels ToF depth camera
    IMU
  Others:
    Tethered
    USB and DisplayPort protocols
    Supports stereo display

## Slide 6: Sensor Decision
STMicroelectronics VL53L5CX
  Resolution: 8 x 8 (=64) pixels
  Range: 2 cm to 400 cm
  FoV: (Horizontal and Vertical)
  Sample rate: 15 FPS at 8 x 8 pixels
Pros of using ToF:
  Eliminate background noise
  Detect motions perpendicular to the image plane

## Slide 7: Overview
Notes: 兩種座標系統對應/校正
手部資訊:手指彎曲程度,手部rotation x y z資訊

## Slide 8: Method
Notes: Mediapipe 基於camera拍到的照片
搭配多媒體機器學習應用辨識手上的landmark
mediapipe是利用 2.5D representation Google團隊使用了一種近似3D hand pose的方法：一樣預測關鍵點在影像上的2D位置，並且額外預測各個關鍵點的相對深度 (local depth)，即相對某個關鍵點的深度差。在大部分的情況下，手腕處或是手掌中心會被設為相對深度的基準點，也就是這個位置的深度視為零。這種表示相對深度的方法被統稱為2.5D表示法。
留言
接下來的問題變成2.5D表示法要怎麼近似真實3D位置。回想一下現在有的資訊：(1) 各個關鍵點在影像上的2D位置、與 (2) 各個關鍵點的相對深度。這時候只要再假設 (3) 手骨長度，將2D的預測與相對深度以幾何投影方式投到3D空間，並放置在手骨長度恰好等於假設值的3D位置上，這樣就完成了3D手姿態的近似。

## Slide 9: Method
To determine the degree of curvature for each finger:
Thumb: Utilize landmarks 0-1 as one pair and 3-4 as another pair.
Index finger: Assess curvature using landmarks 0-6 as one pair and 7-8 as another pair.
Middle finger: Determine curvature based on landmarks 0-10 as one pair and 11-12 as another pair.
Ring finger: Evaluate curvature using landmarks 0-14 as one pair and 15-16 as another pair.
Pinky finger: Measure curvature by utilizing landmarks 0-18 as one pair and 19-20 as another pair.
Calculate the angle between two vectors.

## Slide 10: Method-Rotation
Use (0 5), (5 9) two sets of vectors as reference vector references

## Slide 11: Method-Rotation
Rotation X usese vector (0,9) to calculate the angle between it and (0,1,0) (rotation of the palm)
Rotation Y usese vector (5,9) to calculate the angle between it and (1,0,0)(hand turn left/right)

## Slide 12: Problem of rotation z
The z-coordinate given by Mediapipe is the front and back of each point relative to the wrist, but the value is small and difficult to use

## Slide 13: solution
When hand puts vertical, the distance from the wrist to the finger (0,9) can be used to judge the rotation z
But other methods are needed when hand puts horizontally
When hand puts horizontal , the angle between between (0,5) and (0,17) this two vector
can convert to rotation z

## Slide 14: Future work
Use TOF to determine whether the hand is forward or backward
Work on unity instead of python
More precious
Depth of each finger judgment

## Slide 15: Test
Method: Mediapipe + TOF
Step: Camera -> Mediapipe model + TOF information -> Reconstruct hand in Unity
Result: Finger curving is now functioning correctly, but rotation still needs to be fixed.