## Slide 1
Presenter: Hao-Hsuan Ting (丁浩軒)
Tel: 0972332008
E-mail: r12944052@ntu.edu.tw
Advisor: Prof. Chiou-Shann Fuh
LinFusion: Millimeter Wave Radar and Color Camera Fusion
for People Tracking

## Slide 2
Outline
Introduction
Methodology
Experimental Results
Application
Conclusion

## Slide 3
Introduction

## Slide 4
Jorjin MT5A61E01K
77GHz MMW sensor application kit
Introduction (1/5) – mmWave Radar
FP: False Positive
FN: False Negative
FOV: Field of View
mmWave: Millimeter Wave
Advantages:
Spatial Position
Large FOV
Disadvantages:
“Blind” to still targets
FP or FN are easy to occur when detecting targets
Classification
Notes: 優點：
具有空間位置(距離, 方位角)，速度，加速度。
FOV 比較大，120度。
缺點：
無法識別靜止中的人，也是因為它的特性(基於多普勒效應，只能偵測到相對移動中的物件)
在追蹤目標時，容易出現FP(誤報/鬼影/無中生有) /追蹤失敗的情況，特別是人在交叉經過的時候可能發生。
還有FN(漏報，雷達點消失) /追蹤失敗，即無法追蹤到目標，這種情況多發生與人交叉進過、遮擋、靜止時。
無法分類, 窗簾、風扇、不小心碰撞到物體，都有幾率產生被偵測到。
如圖是我們使用的是Jorjin的device
FP: 誤報/鬼影，FN: 漏報
基於多普勒效應原理，雷達傳送電磁波訊號，其路徑上的物體反射該訊號，透過捕獲反射的訊號，可以確定物體的spatial pos 和 Velocity info.
High-accurate: 高頻->波長短
77GHZ是目前主流車載的高分辨率radar頻段GHZ(GigaHertz) = 109Hz
Ref:
https://www.jorjin.com/products-zh-hant/wireless-connectivity-product-zh-hant/sensing-solution-zh-hant/mmwave-radar/?lang=zh-hant
https://zhuanlan.zhihu.com/p/412722096

## Slide 5
Introduction (2/5) – Color Camera
Advantages:
Features of the target
Rich image information
Disadvantages:
No depth information
Small FOV
FOV: Field of View
Notes: 優點：
相對MMW來說彩色相機擁有豐富的影像資訊和目標的特征，
我們能夠利用DL中multiple object detection and tracking的方法，
對影像中的人進行比較精準的偵測和追蹤。
缺點：
沒有深度資訊，也就是沒有目標的空間位置。
它的FOV較小，只有60度。

## Slide 6
Feature | mmWave Radar | Color Camera
Resolution | Low | High
Velocity Measure | Yes | No
Field Of View | 120° | 60°
Sampling Speed | Low (16FPS) | High (30 FPS)
Environmental Suitability | Good | Bad
Sensor Size | Small | Small
Detection Range | High | Low
Human Detection | “Blind” to Standing Object | Yes
Introduction (3/5) – Comparison
Notes: 我們可以發揮兩個sensor各自的優勢，解決各自的局限性。
Camera 大概是30fps, MMW是16fps。

## Slide 7
Introduction (4/5) – Problem: People Still
Notes: 我們遇到的問題：這邊是幾個毫米波雷達的缺點，或者說限制。
MMW基於多普勒效應，無法識別靜止中的人，只能偵測到相對移動中的object
基於多普勒效應原理，雷達傳送電磁波訊號，其路徑上的物體反射該訊號，透過捕獲反射的訊號，可以確定物體的spatial pos 和 Velocity info.
High-accurate: 高頻->波長短
77GHZ是目前主流車載的高分辨率radar頻段GHZ(GigaHertz) = 109Hz
Ref:
https://www.jorjin.com/products-zh-hant/wireless-connectivity-product-zh-hant/sensing-solution-zh-hant/mmwave-radar/?lang=zh-hant
https://zhuanlan.zhihu.com/p/412722096

## Slide 8
Introduction (4/5) – Problem: mmWave FP
FP: False Positive
mmWave: Millimeter Wave
Notes: 畫面中可以看到，出現 鬼影/ 無中生有 的情況，

## Slide 9
Introduction (4/5) – Problem: mmWave Tracking failed
mmWave : Millimeter Wave
Notes: 畫面中可以看到，因為遮擋，導致 MMW追蹤失敗，導致ID switch，產生新的點。
因為無法判定前後的點是同個人，所以會產生多個毫米波雷達點，特別是人在交叉經過的時候可能發生。

## Slide 10
Introduction (4/5) – Problem: mmWave Tracking failed
mmWave : Millimeter Wave
Notes: 主要是因為遮擋導致的追蹤失敗，並且短暫失去目標的位置(雷達點消失，偵測不到目標)。
這種情況多發生與人交叉進過、被遮擋時。

## Slide 11
Introduction (4/5) – Problem: Summary
mmWave Radar:
  Low tracking accuracy (People Still, Occlusion, Cross)
The Fusion of two sensors:
  The Coordinate System is different.
  The Sampling Rate is different.
  The FOV is different
FOV: Field of View
mmWave : Millimeter Wave
Notes: 毫米波雷達：追蹤能力弱。尤其是People Still, Occlusion, Cross
兩個sensor fusion:
坐標系不一樣。
採樣頻率不一樣。
FOV不一樣。

## Slide 12
Introduction (5/5) – Target
mmWave : Millimeter Wave
Perfectly Fusing everyone in the Camera and mmWave Radar.
Keep the UID unchanged.
  Camera FOV: 60°
  mmWaveRadar FOV: 120°
Notes: 1. 完美融合毫米波雷達和相機中的每個人。
2. 在兩個senor的偵測範圍內，保持UID不變，加強我們的追蹤能力。因為不同FOV，但仍需保持UID不變

## Slide 13
Methodology

## Slide 14
Trained On MOT17 YOLOX detector and ByteTrack tracking algorithm
YOLO: You Only Look Once
MOT: Multiple Object Tracking
Methodology (1/8) – Multiple Object Tracking
Notes: Calculate Transform Function/Matrix
(project mmwave pts to img, meter to pixel)

## Slide 15
We trained a regression model to predict the BBOX centroid.
Input: mmWave (Px, Py, Vx, Vy, Ax, Ay)
Output: BBOX Centroid (x, y)
Methodology (2/8) – Coordinate Calibration
mmWave Radar
Camera
R-C model
R-C: Radar to Camera
BBOX: Bounding box
mmWave: Millimeter Wave
Notes: 我們訓練了一個regression的model，將毫米波雷達點 投影至 影像BBOX的質心。
我們經過實驗後發現利用 更多的資訊 相較於 僅利用 坐標點，精度會高很多。
因此input為毫米波雷達點的px, py, vx, vy, ax, ay。
Output為BBOX質心。
在得到有毫米波雷達點預測出的pixel point後，
我們可以與 目標 進行匹配。

## Slide 16
Methodology (3/8) – Position Estimation
mmWave Radar
Camera
C-R model
C-R: Camera to Radar
BBOX: Bounding box
mmWave: Millimeter Wave
We trained a regression model to predict the real position.
Input: BBOX center bottom (x, y)
Output: mmWave (Px, Py)
Notes: 這邊提出了一個基於Ml的方法 利用 BBOX資訊 來預測 空間位置 。
這樣做的優點/目的：
影像中的人在沒有對應的毫米波雷達點時(人靜止/MMW追蹤失敗)，可以採用估計的位置
為後續 毫米波雷達 與 彩色相機 的融合提供更多資訊，提升融合的精度(特別是交叉經過、遮擋的時候，深度資訊是有幫助的)。
我們觀察BBOX中心底部的點是相對穩定，且和真實位置有一定的關係的(perspective transform)。
因此我們將中心底部點作為input，output為空間真實位置。

## Slide 17
Methodology (4/8) – Dataset Collection
mmWave Radar
Camera
Auto Labeling: when there is only one person in the image and only one point in the mmWave radar.
mmWave: Millimeter Wave
Notes: 為了更加方便收集data來訓練前面的模型，減少標註data的時間，
我們設定 當圖像中只有一個人，毫米波雷達中只有一個點時，
將這對data自動匹配，達到自動標註的效果。
再分別應用到前面 坐標校正 和 位置估計 的ml model中進行訓練。

## Slide 18
Methodology (5/8) – Target Fusion
mmWave: Millimeter Wave
R-C: Radar to Camera
C-R: Camera to Radar
mmWave Radar
Camera
R-C model
Predict
Centroid
mmWave Radar
Camera
C-R model
Predict
Position
Coordinate Calibration
Position Estimation
Notes: 如圖分別是 坐標校正 和 位置估計 的兩個結果圖。
所以我們可以比較 pixel點之間的距離 與 位置之間的距離，來判斷是否匹配。

## Slide 19
  Given: 2 pairs of lists:
    mmWave list: x’, y’, Px, Py
    BBOX list: x, y, Px’, Py’
  Match the 2 pairs of lists:
    Calculate the Error Matrix (m*n)
      if (x’, y’) is outside the BBOX  unmatched
    Match Algorithm  Hungarian Algorithm
      Matches, Unmatched mmWave, Unmatched BBOX
      Unmatched BBOX  Use Estimated Position in radar image
Methodology (5/8) – Target Fusion
mmWave: Millimeter Wave
BBOX: Bounding box
Notes: 經過我們前面的方法，我們 現在的已知資訊有 mmw and Cam.
我們計算他們之間的歐式距離，可以得到centroid 和 position distance error.
因為兩個distance之間的單位不一樣，所以我們會給定一個權重，目前是1， 100。
我們會先經過預處理，把不在BBOX內的 毫米波雷達點 排除在外。
然後將計算出的error matrix 透過 Hungarian 進行匹配，會得到三類。
其中 unmatched BBOX 我們可以使用 預測出的位置 來 代替 毫米波雷達點。

## Slide 20
Methodology (6/8) – UID Assignment Strategy
The smaller blue angle indicates the FOV of the color camera. (overlapping area of sensors)
The larger red angle indicates the FOV of the mmWave radar.
FOV: Field Of View
mmWave: Millimeter Wave
Notes: 如圖是我們主要的實驗區域，藍色線是我們的camera範圍，紅色是mmw範圍

## Slide 21
Methodology (6/8) – UID Assignment Strategy
mmWave
CAM
START
UID MID
UID CID MID
UID CID
STATE:
mmWave
CAM
STATE:
Match
Match
Match
UID MID
UID CID MID
UID CID
UID CID MID
Outside
overlapping
area
Outside
overlapping
area
In the
overlapping
area
In the
overlapping
area
mmWave
MID
ID List:
ID List:
In the
overlapping
area
Our Strategy: CID dominates.
NOTE: CID is incremental, MID is complementary.
CAM: Camera
BBOX: Bounding Box
mmWave: Millimeter Wave
UID: Unique IDentifier
CID: Camera IDentifier
MID: mmWave IDentifier
Notes: 這邊要介紹我們的UID策略，目的是為了在兩個sensor傳感器範圍內保持ID不變。
已知我們在 camera端 和 MMW端 都會有追蹤結果，得到CID, MID, 其中CID是遞增，MID是遞補的，遞補的MID會對後續持續追蹤影響很大，
並且在影像端的追蹤精度是高於MMW的，因此我們的策略是CID主導，MID為輔助。
UID分配：在only MMW area，分配一個UID。 在overlapping area，不會給MMW assign UID, 會給每個BBOX一個UID。
狀態的轉變：
MMW to Match: 從重疊區域外走進內。
Match to MMW: 內走到外。
Match to CAM： 在重疊區域內，沒有match到MMW (遮擋，站立，無法偵測)。
CAM to Match: 找到對應MMW。
困難點：
從只有毫米波雷達區域 走進 重疊區域
從重疊區域 走進只有雷達的區域
這幾種條件下，要保持UID不變。

## Slide 22
Methodology (7/8) – Current System Flow Chart
Camera
mmWave
BBOX info
Centroid,
Estimated Position
mmWave info
ByteTrack
Estimated Centroid,
Real Position
Time Synchronization
Pixel, meter
Pixel, meter
Calculate
Error
Camera-Radar
Regression model
Radar-Camera
Regression model
Hungarian Algorithm
BBOX: Bounding box
mmWave: Millimeter Wave
Position Estimation
BBOX Centroid Estimation
Match Person & mmWave
Unmatched BBOX/Person
Unmatched mmWave

## Slide 23
If Outside overlapping area
Methodology (7/8) – Current System Flow Chart - UID
Hungarian Algorithm
BBOX: Bounding Box
UID: Unique IDentifier
mmWave: Millimeter Wave
Match Person & mmWave
Unmatched BBOX/Person
Unmatched mmWave
Assign a UID
Assign a UID
Assign a UID
UID MID
UID CID MID
UID CID
UID: Unique IDentifier
CID: Camera IDentifier
MID: mmWave IDentifier

## Slide 24
Methodology (8/8) – Time Synchronization
Tcamera > Tradar: Use extrapolation (Uniform Acceleration)
Tradar
Tcamera
Notes: 因為兩個sensor不同的採樣頻率，Camera 大概是30fps, MMW是16fps。
所以我們需要對他們進行時間同步，理論上來說他們的資訊會更加準確。
當camera 時間快於Radar時，我們會用勻加速公式來同步camera時間點的radar 數值。

## Slide 25
Methodology (8/8) – Time Synchronization
mmWave: Millimeter Wave
[x, y, vx, vy, ax, ay]
mmWave radar data
After Time Synchronization
Matrix Form
Tcamera > Tradar: Use extrapolation (Uniform Acceleration)
Uniform
Acceleration
Notes: 因為radar本身有x, y, vx, vy, ax, ay，所以剛好可以利用勻加速公式進行同步。

## Slide 26
Methodology (8/8) – Time Synchronization
Tcamera < Tradar : Use Linear Interpolation method
Tcamera
Tradar
Linear Interpolation Equation
Notes: 當相機採樣的時間慢於毫米波雷達時，我們會使用線性內插的方法。
t (current image timestamp), x (millimeter-wave radar information of the target),
x1 and t1 (the current millimeter-wave radar information and its corresponding timestamp),
x0 and t0 (represent the previous millimeter-wave radar information and its corresponding timestamp).

## Slide 27
Experimental Results

## Slide 28
Experimental Results (1/5) – Environment
Camera
mmWave Radar
Camera
mmWave Radar
mmWave: Millimeter Wave
Lab 328
1
2
Notes: 如圖是我們在LAB328空間時測試時，sensor架設的位置。

## Slide 29
Experimental Results (1/5) – Environment
Camera
mmWave Radar
mmWave: Millimeter Wave
Lab 326
4
3
Camera
mmWave Radar
Notes: 在LAB326時，sensor架設的位置。

## Slide 30
Experimental Results (2/5) – Dataset
mmWave: Millimeter Wave
NO. | Training (frames) | Testing (frames)
1 | 1,322 | 6,534
2 | 1,848 | 8,074
3 | 1,192 | 4,801
4 | 1,387 | 3,784
30 frames/second
Notes: 我們收集了在上述4個sensor架設位置下的data。
1, 2在Lab 328
3, 4在lab326
Unit: frame

## Slide 31
Experimental Results (3/5) – Coordinate Calibration
mmWave Radar
Camera
R-C model
Predict
Centroid
R-C: Radar to Camera
MSE: Mean Squared Error
mmWave: Millimeter Wave
Metric
Notes: 這邊我們測試 坐標校正 方法的精度。
Metric: MSE，兩點之間的距離 (pixel)。

## Slide 32
Experimental Results (3/5) – Coordinate Calibration
R-C: Radar to Camera
MSE: Mean Squared Error
mmWave: Millimeter Wave

## Slide 33
Experimental Results (3/5) – Coordinate Calibration
Dataset Type | Quantity | Linear Transform | ML model (ours)
Training | 1,322 | 63.339 | 25.309
Testing | 6,005 | 43.796 | 22.480

Dataset Type | Quantity | Linear Transform | ML model (ours)
Training | 1,848 | 45.812 | 25.004
Testing | 8,939 | 51.489 | 27.360
1
2

Calibration Error (Pixels)
Notes: Metric: MSE 兩點之間的距離。
pixel

## Slide 34
Experimental Results (3/5) – Coordinate Calibration
Dataset Type | Quantity | Linear Transform | ML model (ours)
Training | 1,192 | 44.908 | 19.217
Testing | 5,473 | 56.626 | 23.840

Dataset Type | Quantity | Linear Transform | ML model (ours)
Training | 1,387 | 48.603 | 11.715
Testing | 5,818 | 49.314 | 22.868
3
4

Calibration Error (Pixels)
Notes: Metric: MSE 兩點之間的距離。
pixel

## Slide 35
Experimental Results (4/5) – Position Estimation
Metric
mmWave Radar
Camera
C-R model
Predict
Position
C-R: Camera to Radar
MSE: Mean Squared Error
mmWave: Millimeter Wave
Notes: 測試 位置估計 方法的精度。
Metric: MSE，兩點之間的距離(meter)。

## Slide 36
Experimental Results (4/5) – Position Estimation
C-R: Camera to Radar
MSE: Mean Squared Error
mmWave: Millimeter Wave

## Slide 37
Experimental Results (4/5) – Position Estimation
C-R: Camera to Radar
MSE: Mean Squared Error
mmWave: Millimeter Wave
Dataset Type | Quantity | MSE 
Training | 1,322 | 0.2030
Testing | 6,005 | 0.1953
1
2
Dataset Type | Quantity | MSE 
Training | 1,848 | 0.188
Testing | 8,939 | 0.2253
Position Error (Meters)

## Slide 38
Experimental Results (4/5) – Position Estimation
C-R: Camera to Radar
MSE: Mean Squared Error
mmWave: Millimeter Wave
Dataset Type | Quantity | MSE 
Training | 1,192 | 0.318
Testing | 5,473 | 0.233
3
4
Dataset Type | Quantity | MSE 
Training | 1,387 | 0.184
Testing | 5,818 | 0.230
Position Error (Meters)

## Slide 39
Experimental Results (5/5) – UID
Situation | UID Switch 
BBOX Switch | 15
mmWave Tracking Fail | 30
Total | 45
BBOX: Bounding Box
UID: Unique IDentifier
mmWave: Millimeter Wave
Totally: 28,942 frames = 965 seconds
Fusion mmWave Only Camera Only
Notes: Metric: ID switch

## Slide 40
Experimental Results (5/5) – UID
Visualization…
UID: Unique IDentifier

## Slide 41
Application

## Slide 42
Application (1/2)
Scenario: 3m*3m square region
Height: 2.4 m

## Slide 43
Application (2/2)
Visualization…

## Slide 44
Conclusion
Method: Deep learning-based coordinate calibration and spatial position estimation methods to improve fusion accuracy.
Step: Time synchronization on two sensors’ input data -> Position Estimation & Coordinate Calibration -> UID Assignment based on Hungarian Algorithm
Result: This system maintains consistent IDs for targets within the range of both sensors.
mmWave: Millimeter Wave

## Slide 45
Thanks!!!