## Slide 1: 3D MMWave for Gesture Recognition
Presenter: Hao-Hsuan Ting 丁浩軒
Tel: 0972-332008
E-mail: r12944052@ntu.edu.tw
Advisor: Prof. Chiou-Shann Fuh 傅楸善

## Slide 2: Outline
Introduction
Methodology
Conclusion

## Slide 3: Introduction
Texas Instrument IWR6843 MMWave sensor
Industrial sensors for measuring range, speed, and angle
Gesture recognition
Position sensing
People counting
Motion detection

## Slide 4: Introduction
People counting
Spatial position and speed

## Slide 5: Introduction
Raw output data is represented in polar coordinates.
The angular resolution is 0.01 radians
  Both Elevation and Azimuth

## Slide 6: Introduction
MMWave Resolution
Elevation ranges from -0.34 to 0.34 radian (-19.48° to 19.48°)
  The missing angles include -0.32, ±0.25, ±0.23, ±0.18, ±0.16, ±0.13, ±0.11, ±0.04, and ±0.01 radian
Azimuth ranges from -1.28 to 1.27 radian (-73.338° to 72.766°)
  No missing angle

## Slide 7: Introduction
MMWave Resolution
We can use elevation and azimuth to generate a 69 pixels * 256 pixels image
  This image is generated by accumulating point cloud, not real-time point cloud
Notes: 越近越紅

## Slide 8: Methodology
2D Heat map De-noising
Histogram

## Slide 9: Methodology
2D Heat map De-noising
There are many noises points in output data
Closing operation
Opening operation
Median Blur
Gaussian Blur

## Slide 10: 2D Heat map De-noising
2D Heat map De-noising
Keep two images: one is binary image, other is gray-level image
Binary image: pixel = 255 if there is any point in this pixel
Gray-level image: pixel = 255 * (range_of_point - 0.5) / (3-0.5)

## Slide 11: 2D Heat map De-noising
2D Heat map De-noising
Keep two images: one is binary image, other is gray-level image
Binary image: pixel = 255 if there is any point in this pixel
Gray-level image: pixel = 255 * (range_of_point - 0.5) / (3-0.5)
Do Dilation first and then do Erosion to complement the lack of pixel
  Manipulate two images separately

## Slide 12: 2D Heat map De-noising
Opening operation
Do dilation twice and then do erosion twice
  Kernel (3 by 3) is too big for image, so do these twice
Do opening operation on two images separately
After opening
  If pixel = 0 in binary image, set pixel = 0 in gray-level image
  Else pixel in gray-level image does not change

## Slide 13: 2D Heat map De-noising
Median Blur – Method 1
The median blur effect is similar to the erosion effect
Do dilation and then do erosion
Do median blur on gray-level image three times
  Why do it three times? The best de-noising effect
Finer, more detail => better than opening

## Slide 14: 2D Heat map De-noising
Median Blur – Method 2
The median blur effect is similar to the erosion effect
Do dilation and then do erosion
Do median blur on binary image three times for de-noise
Do median blur on gray-level image one time for pixel value expansion
After blurring
  If pixel = 0 in binary image, set pixel = 0 in gray-level image
  Else pixel in gray-level image does not change

## Slide 15: 2D Heat map De-noising
Median and Gaussian Blur – Method 3
The median blur effect is similar to the erosion effect
Do dilation and then do erosion
Do median blur on binary image three times for de-noise
Do Gaussian blur on gray-level image one time for pixel value expansion
After blurring
  If pixel = 0 in binary image, set pixel = 0 in gray-level image
  Else pixel in gray-level image does not change

## Slide 16: 2D Heat map De-noising
Comparison
Image from top to bottom respectively is
  Method 3: Gaussian blur
  Method 2: median blur
  Method 1: 3 times of median blur
  Opening
  Raw image
Notes: 9-30
提到第二張中間空缺沒有被填滿

## Slide 17: 2D Heat map De-noising
Comparison
Image from top to bottom respectively is
  Method 3: Gaussian blur
  Method 2: median blur
  Method 1: 3 times of median blur
  Opening
  Raw image
Notes: 182
提到第三張有黑色pixel

## Slide 18: 2D Heat map De-noising
Comparison
Image from top to bottom respectively is
  Method 3: Gaussian blur
  Method 2: median blur
  Method 1: 3 times of median blur
  Opening
  Raw image
Notes: 314

## Slide 19: 2D Heat map De-noising
Comparison
Image from top to bottom respectively is
  Method 3: Gaussian blur
  Method 2: median blur
  Method 1: 3 times of median blur
  Opening
  Raw image
Notes: 555
一樣，空缺並沒有填滿太多

## Slide 20: 2D Heat map De-noising
Comparison
Image from top to bottom respectively is
  Method 3: Gaussian blur
  Method 2: median blur
  Method 1: 3 times of median blur
  Opening
  Raw image
Notes: 677
顏色沒有擴散太多

## Slide 21: 2D Heat map De-noising
Comparison
Image from top to bottom respectively is
  Method 3: Gaussian blur
  Method 2: median blur
  Method 1: 3 times of median blur
  Opening
  Raw image
Notes: 694
空缺

## Slide 22: 2D Heat map De-noising
Comparison
Method 3: Gaussian blur
  The blurred pixel value is not good
Method 2: median blur once
  I think this is the best one and quicker
Method 1: 3 times of median blur
  Also great, but the detail is worse than one-time method and slower
Opening operation
  No detail

## Slide 23: Histogram
Calculate histogram on gray-level image
Pick up the point in range
[minimum non-zero pixel value: minimum non-zero pixel value +15]
At beginning, we set the point range within range: 250 cm = 300 – 50 cm
  250 cm almost can map onto 256 pixels
  15 pixel value equals to 14.6 cm, one hand size
  15 cm: hand at the shortest distance, 15 cm to remove body and other points as noise
Can detect one hand in mmwave sensor range
Can detect more than one hand, but must wave at the same distance

## Slide 24: Conclusion
Method
  Enhance the clarity of hand-waving motion in 2D heat map by image processing method.
Step
  Convert mmwave output data to 2D heat map
  Use opening and closing and median blur to de-noise the heat map
  Highlight hand information using histogram.
Result
  Can detect one hand in mmwave sensor range.