## Slide 1
Presented by: 傅楸善教授 & 李志洸
0972498002
yaolin45040@gmail.com
Advanced Computer Vision
Chapter 2
Image Formation

## Slide 2: Image Formation
2.1 Geometric primitives and transformations
2.2 Photometric image formation
2.3 The digital camera
Notes: Photometric 光度學

## Slide 3: Image Formation
Notes: Perspective projection 透視投影 <-> Orthography projection 平行投影

## Slide 4: 2.1 Geometric Primitives and Transformations
2.1.1 Geometric Primitives
2.1.2 2D Transformations
2.1.3 3D Transformations
2.1.4 3D Rotations
2.1.5 3D to 2D Projections
2.1.6 Lens Distortions
Notes: Distortions 失真

## Slide 5: 2.1.1 Geometric Primitives
Simplest geometric objects used to describe 2D and 3D shapes.
Points, Lines and Planes.
Notes: Distortions 失真

## Slide 6: 2.1.1 Geometric Primitives
2D points (pixel coordinates in an image)
  .
  Homogeneous coordinates:
    A system of coordinates used in projective geometry.
    : 2D projective space, .
    (tx, ty, t) = (x, y, 1) in homogeneous coordinate.
    Augmented vector .
Notes: Homogeneous coordinates 齊次座標
如果最後一個值為0 則代表 ideal points(理想點) or points at infinity(無窮遠點)
原點是 (0, 0, 1)
Augmented vector 擴充特徵向量

## Slide 7: 2.1.1 Geometric Primitives
2D lines
  , where .
  Normalize the line equation vector:
    with .
    is the normal vector.
    | is the distance to the origin.
Notes: 是內積
法向量
¯𝒙∙𝒍 ̃ 是內積
𝒏 ̂ 法向量

## Slide 8: 2.1.1 Geometric Primitives
2D conics: circle, ellipse, parabola, hyperbola
  Q
  Quadric equation: .
Notes: Conics 圓錐曲線
Ellipse 橢圓
Parabola 拋物線
Hyperbola 雙曲線
Quadric equation 二次型方程式

## Slide 9: 2.1.1 Geometric Primitives
3D points:
  Homogeneous coordinates:
  Augmented vector:

## Slide 10: 2.1.1 Geometric Primitives
midpoint
3D lines:
  Two points on the line, .
  Any other point on the line can be expressed as a linear combination of these two points.

## Slide 11: 2.1.1 Geometric Primitives
3D planes:
  where .
  Normalize the plane equation: with .
    is the normal vector.
    | is the distance to the origin.

## Slide 12: 2.1.1 Geometric Primitives
3D quadrics:
  Spheres, Ellipsoids, Cylinders
Parabolic cylinder
Sphere
Ellipsoid
Circular cylinder
Elliptic cylinder
Hyperbolic cylinder
Notes: Quadrics 二次曲面
Cylinder 圓柱體
Elliptic 橢圓的
Parabolic 拋物線

## Slide 13: 2.1.2 2D Transformations
Preserves | Translation | Euclidean | Similarity | Affine | Projective
Lengths | O | O | X | X | X
Angles | O | O | O | X | X
Parallelism | O | O | O | O | X
Notes: 轉換(位移)、歐基里德(旋轉+位移)、相似、仿射、投影

## Slide 14: 2.1.2 2D Transformations
Translation
  2D translations can be written as or .
  Augmented vector:

## Slide 15: 2.1.2 2D Transformations
Euclidean
  Rotation + Translation.
  Also known as 2D rigid body motion.
  or
  R is an orthonormal rotation matrix with and .
    orthonormal matrix: .
Notes: 鋼體運動
逆時針選轉 度
orthonormal正規化
鋼體運動
逆時針選轉 𝜃 度

## Slide 16: 2.1.2 2D Transformations
Similarity
  Scaled Rotation.
  s: an arbitrary scale factor

## Slide 17: 2.1.2 2D Transformations
Affine
  , where is an arbitrary 2 × 3 matrix.
  Preserves parallelism:
    Square  Parallelogram
    Parallelogram  Parallelogram

## Slide 18: 2.1.2 2D Transformations
Projective
  2D Projective operates on homogeneous coordinates ,
  Also known as perspective transform or homography.
  Preserves straight lines:
    Square  arbitrary quadrilateral
    Straight lines  straight lines
Notes: perspective transform 透視轉換
Homography 單應性
arbitrary quadrilateral 多變的四邊形

## Slide 19: 2.1.2 2D Transformations
Hierarchy of 2D coordinate transformations. Each transformation also preserves the properties listed in the rows below. The 2 X 3 matrices are extended with a third [0 0 1] row to form a full 3 X 3 matrix.

## Slide 20: 2.1.3 3D Transformations
The 3D transformations are similar to the 2D transformations.

## Slide 21: 2.1.4 3D Rotations
Axis/Angle
  A rotation can be represented by a rotation axis and an angle .
  Or equivalently by a 3D vector .

## Slide 22: 2.1.4 3D Rotations
Project the vector onto the axis :
Compute the perpendicular residual of from :
Rotate this vector by 90◦ using the cross product:
  Where is the matrix form of cross product operator with the vector .
Notes: Perpendicular 垂直的
Residual 分量

## Slide 23: 2.1.4 3D Rotations
Rotate this vector by another 90◦:
Compute the in-plane component of the rotated vector
Obtain the final rotated vector:
Rodriguez’s formula:
Notes: Perpendicular 垂直的
Residual 分量

## Slide 24: 2.1.5 3D to 2D Projections
We need to specify how 3D primitives are projected onto the image plane.
The simplest model is orthography, and the more commonly used model is perspective.
vanishing point

## Slide 25: 2.1.5 3D to 2D Projections
Orthography
  An orthographic projection simply drops the z component of the 3D coordinate 𝒑 to obtain the 2D point 𝒙.
Homogeneous (projective) coordinates:
In practice, world coordinates need to be scaled to fit onto an image sensor. For this reason, scaled orthography is actually more commonly used.

## Slide 26: 2.1.5 3D to 2D Projections
Perspective
  The most commonly used projection in computer graphics and computer vision is true 3D perspective.
Points are projected onto the image plane by dividing them by their z component.

## Slide 27: 2.1.5 3D to 2D Projections
Perspective vs. Orthography

## Slide 28: 2.1.5 Camera Intrinsics
A camera is a mapping between the 3D world and a 2D image
Notes: Intrinsics 內部參數
Nodal point 節點

## Slide 29: 2.1.5 Camera Intrinsics
The pinhole camera
camera center
X
image plane
principal axis
y
principal point
Notes: Intrinsics 內部
principal point 主點
Pinhole camera 針孔相機

## Slide 30: 2.1.5 Camera Intrinsics
Image plane
X
Y
Z
f
fY
Z
[X Y Z]T  [f X/Z fY /Z]T

## Slide 31: 2.1.5 Camera Intrinsics

## Slide 32: 2.1.5 Camera Intrinsics
Camera origin and image origin might be different
camera coordinate system
image coordinate system
CCD array
p
Accounts for different origins

## Slide 33: 2.1.5 Camera Intrinsics
Can be decomposed into two matrices
Notes: K is called the calibration matrix and describes the camera intrinsics

## Slide 34: 2.1.5 Camera Intrinsics
xc
yc
zc
zw
xw
yw
World coordinate system
Camera coordinate
system
Xw
C
Xc
Rotate
R
(Xw — C)

## Slide 35: 2.1.5 Camera Intrinsics

## Slide 36: 2.1.5 Camera Intrinsics: A note on Focal Lengths
Notes: Focal length 焦距

## Slide 37: 2.1.6 Lens Distortions
Imaging models all assume that cameras obey a linear projection model where straight lines in the world result in straight lines in the image.
Many wide-angles lenses have noticeable radial distortion

## Slide 38: 2.2 Photometric Image Formation
2.2.1 Lighting
2.2.2 Reflectance and shading
2.2.3 Optics

## Slide 39: 2.2.1 Lighting
To produce an image, the scene must be illuminated with one or more light sources.

## Slide 40: 2.2.1 Lighting
A point light source has an intensity and a color spectrum, i.e., a distribution over wavelengths .

## Slide 41: 2.2.2 Reflectance and Shading
Bidirectional Reflectance Distribution Function (BRDF)
  BRDF describes how much of each wavelength arriving at an incident direction is emitted in a reflected direction .
  The angles of the incident and reflected directions relative to the surface frames as .

## Slide 42: 2.2.2 Reflectance and Shading
Diffuse Reflection and Specular Reflection
  Diffuse Reflection: The diffuse component scatters light uniformly in all directions.
  Specular Reflection: Incident light rays are reflected in a direction that is rotated by 180◦ around the surface normal .
Diffuse Reflection
(rough surfaces)
Specular Reflection
(smooth surfaces)
Notes: Diffuse 漫射
Specular 鏡射

## Slide 43: 2.2.2 Reflectance and Shading
Phong combined the diffuse and specular components of reflection with ambient illumination.
Notes: Phong shading Phong 著色法
Ambient illumination 周圍照明

## Slide 44: 2.2.2 Reflectance and Shading
Objects are generally illuminated not only by point light sources but also by a diffuse illumination corresponding to inter-reflection (e.g., the walls in a room) or distant sources, such as the blue sky.
Notes: Phong shading Phong 著色法
Ambient illumination 周圍照明

## Slide 45: 2.2.3 Optics
The light from a scene reaches the camera, it must pass through the lens before reaching the sensor.
The thin lens composed of a single piece of glass with very low, equal curvature on both sides.
Notes: Phong shading Phong 著色法
Ambient illumination 周圍照明

## Slide 46: 2.2.3 Optics
Vignetting
  The tendency for the brightness of the image to fall off towards the edge of the image.
Notes: Vignetting 暈影
處理方法是拍一張全白的畫面，最暗的地方除以最白的地方，形成一個矯正用的陣列

## Slide 47: 2.3 The Digital Camera
2.3.1 Sampling and aliasing
2.3.2 Color
2.3.3 Compression

## Slide 48: 2.3 The Digital Camera
CCD: Charge-Coupled Device
CMOS: Complementary Metal-Oxide-Semiconductor
A/D: Analog-to-Digital Converter
DSP: Digital Signal Processor
JPEG: Joint Photographic Experts Group
ISO: International Standards Organization
Notes: Optics 光學
Aperture 光圈

## Slide 49: 2.3 The Digital Camera
CCD (Charge-Coupled Device)
  Photons are accumulated in each active well during the exposure time.
  In a transfer phase, the charges are transferred from well to well in a kind of “bucket brigade” until they are deposited at the sense amplifiers.
Notes: Charge-Coupled device 電荷耦合元件
Photon 光子
Well 井
Bucket brigade 桶 旅(軍人) 依序裝載的容器

## Slide 50: 2.3 The Digital Camera
CMOS (Complementary Metal-Oxide-Semiconductor)
  The photons hitting the sensor directly affect the conductivity of a photodetector, which can be selectively gated to control exposure duration, and locally amplified before being read out using a multiplexing scheme.
Notes: Complementary 互補的
Oxide 氧化物
Photodetector 光感測器

## Slide 51: 2.3 The Digital Camera
Shutter speed
  The shutter speed (exposure time) directly controls the amount of light reaching the sensor and determines if images are under- or over-exposed.
Sampling pitch
  The sampling pitch is the physical spacing between adjacent sensor cells on the imaging chip.
Fill factor
  The fill factor is the active sensing area size as a fraction of the theoretically available sensing area (the product of the horizontal and vertical sampling pitches).
Notes: Fill factor 填充因子

## Slide 52: 2.3 The Digital Camera
Chip size
  Video and point-and-shoot cameras have traditionally used small chip areas(1/4-inch to 1/2-inch sensors).
Analog gain
  Before analog-to-digital conversion, the sensed signal is usually boosted by a sense amplifier.
Sensor noise
  Throughout the whole sensing process, noise is added from various sources, which may include fixed pattern noise, dark current noise, shot noise, amplifier noise and quantization noise.
Notes: Point-and-shoot cameras 傻瓜相機
Pattern 圖形
dark current noise 暗電流，沒有光子通過sensor時還會有的微小電流
Shot noise 散粒雜訊
quantization noise 量化雜訊

## Slide 53: 2.3 The Digital Camera
ADC resolution
  Resolution: how many bits it yields
  Noise level: how many of these bits are useful in practice
Digital post-processing
  To enhance the image before compressing and storing the pixel values.
ADC: Analog-to-Digital Converter
Notes: Yields 產生

## Slide 54: 2.3.1 Sampling and Aliasing
Sampling

## Slide 55: 2.3.1 Sampling and Aliasing
Nyquist Frequency
  The minimum sampling rate required to reconstruct a signal from its samples must be at least twice the highest frequency.
The inverse of the minimum sampling frequency is known as the Nyquist rate.
Notes: 奈 quist

## Slide 56: 2.3.1 Sampling and Aliasing
Aliasing

## Slide 57: 2.3.2 Color
Additive Colors:
R + G = Yellow
B + R = Magenta
G + B = Cyan
R + G + B = White
R
G
B
C
M
Y
K
Subtractive Colors:
M + C = Blue
C + Y = Green
Y + M = Red
Y + M + C = black
(a) Additive colors: RGB
(a) Subtractive colors: CMYK

## Slide 58: 2.3.2 Color Additive Colors
Start with Black – absence of any colors. The more colors added, the brighter it gets.
Color formation by the addition of Red, Green, and Blue, the three primary colors
Examples of additive color usage:-
  Human eye
  Lighting
  Color monitors
  Color video cameras
Additive color wheel

## Slide 59: 2.3.2 Color Subtractive Colors
Starts with a white background (usually paper).
Use Cyan, Magenta, and/or Yellow dyes to subtract from light reflected by paper, to produce all colors.
Examples of Subtractive color use:-
  Color printers
  Paints
Subtractive color wheel

## Slide 60: 2.3.2 Color
CIE RGB and XYZ
  In the 1930s, Commission Internationale de L'Eclairage (CIE) standardized the RGB representation by performing such color matching experiments using the primary colors of red (700.0nm wavelength), green (546.1nm), and blue (435.8nm).
CIE: International Commission on Illumination
Figure 2.28 Standard CIE color matching functions: (a) color spectra obtained from matching pure colors to the R=700.0nm, G=546.1nm, and B=435.8nm primaries; (b) color matching functions, which are linear combinations of the spectra.

## Slide 61: 2.3.2 Color
CIE RGB and XYZ
  Because of the problem associated with mixing negative light, the CIE also developed a new color space called XYZ.
  The transformation from RGB to XYZ is given by:
  Chromaticity coordinates

## Slide 62: 2.3.2 Color
Figure 2.29 CIE chromaticity diagram, showing colors and their corresponding (x, y) values. Pure spectral colors are arranged around the outside of the curve.
λ = 380 nm ~
λ = 800 nm

## Slide 63: 2.3.2 Color
L*a*b* Color Space
  CIE defined a non-linear re-mapping of the XYZ space called L*a*b* (also sometimes called CIELAB).

## Slide 64: 2.3.2 Color
L*a*b* Color Space
  The three coordinates of L*a*b* space represent the lightness of the color.
  L*: L* = 0 yields black and L* = 100 indicates white.
  a*: The position between red/magenta (positive values) and green (negative values).
  b*: The position between yellow (positive values) and blue (negative values).

## Slide 65: 2.3.2 Color
Color Filter Arrays (CFA)
  Most of today’s digital still cameras and video cameras use a color filter array (CFA), where alternating sensors are covered by different colored filters.

## Slide 66: 2.3.2 Color
Color Filter Arrays (CFA) – Bayer Pattern
  Green filters are placed over half of the sensors (in a checkerboard pattern), and red and blue filters are placed over the remaining ones.
  The reason that there are twice as many green filters as red and blue is:
    The luminance signal is mostly determined by green values.
    The visual system is much more sensitive to high frequency detail in luminance than in chrominance.
Incoming light
Filter layer
Sensor array
Resulting pattern

## Slide 67: 2.3.2 Color
Color Filter Arrays (CFA) – Bayer Pattern
  The process of interpolating the missing color values so that we have valid RGB values for all the pixels is known as demosaicing (color interpolation).
Notes: 顏色差補

## Slide 68: 2.3.2 Color
Color Balance (Auto White Balance)
  Before encoding the sensed RGB values, most cameras perform some kind of color balancing operation in an attempt to move the white point of a given image closer to pure white.
  If the illuminant is strongly colored, such as incandescent indoor lighting (which generally results in a yellow or orange hue), the compensation can be quite significant.
Notes: Incandescent 熾熱的
Compensation 補償

## Slide 69: 2.3.2 Color
Gamma
  For CRT (Cathode Ray Tube), the relationship between the voltage (V) and the brightness (B) was characterized by gamma (γ), γ=2.2.
  To compensate for this effect, the electronics in the TV camera would pre-map the luminance Y through an inverse gamma, 1/γ = 0.45.
LCD
Camera
Notes: CRT 陰極射線管
Compensate 補償
相機的線性感受亮度會使得影像顯得奇怪
有不同的校正曲線
Gamma 1.0  RAW檔

## Slide 70: 2.3.2 Color
Other Color Spaces
    HSV: hue, saturation, value
      A projection of the RGB color cube onto a non-linear chroma angle, a radial saturation percentage, and a luminance-inspired value.
RGB
HSV

## Slide 71: 2.3.2 Color
Other Color Spaces
  YUV
  Y: luminance (Y’: luma)
  U, V: chrominance
  YCbCr
    Cb, Cr: the blue-difference and red-difference chroma components.
    R’G’B’ values are the eight-bit gamma-compressed color components.

## Slide 72: 2.3.2 Color
Figure 2.32 Color space transformations: (a–d) RGB; (e–h) rgb; (i–k) L*a*b*; (l–n) HSV. Note that the rgb, L*a*b*, and HSV values are all re-scaled to fit the dynamic range of the printed page.

## Slide 73: 2.3.3 Compression
All color video and image compression algorithms start by converting the signal into YCbCr (or some closely related variant), so that they can compress the luminance signal with higher fidelity than the chrominance signal.
In video, it is common to subsample Cb and Cr by a factor of two horizontally; with still images (JPEG), the subsampling (averaging) occurs both horizontally and vertically.
Notes: Fidelity 保真度
Chrominance 色度

## Slide 74: 2.3.3 Compression
Once the luminance and chrominance images have been appropriately subsampled and separated into individual images, they are then passed to a block transform stage.
The most common technique used here is the Discrete Cosine Transform (DCT), which is a real-valued variant of the Discrete Fourier Transform (DFT).
After transform coding, the coefficient values are quantized into a set of small integer values that can be coded using a variable bit length scheme such as a Huffman code or an arithmetic code.
Notes: Chrominance 色度

## Slide 75: 2.3.3 Compression
The step size in the quantization is the main variable controlled by the quality setting on the JPEG file.
JPEG (Joint Photographic Experts Group)

## Slide 76: Homework 2: Project due March 19
1. Camera calibration i.e. compute object displacement(#mm/ pixel )
2. Calculate horizontal field of view in degrees of angle.
3. Calculate theoretical values (FOV) and compare with measured values.
Using the sample images at http://goo.gl/pWBNN0
Use lens of focal length: 18mm, 53mm, 135mm
Object displacement of: 1mm, 5mm, 10mm, 20mm
Object distance of: 0.6m, 1.2m, 1.8m

## Slide 77: Homework 2: Project due March 19
Pentax K-7 相機資訊 https://www.digicamdb.com/specs/pentax_k-7/
Sensor size: 23.4 x 15.6 mm
Notes: Calculate Pixel displacement first

## Slide 78: Homework 2: Project due March 19
FOV theoretical value (f = 135mm, sensor width = 23.4mm):
FOV
FOV measured value:
FOV